## Slide 1
IoT based integrated smart home protocol for wellness sensing and assistive living
THE TEAM MEMBERS
Zhenwei FU
Zhenpeng Wang
Keke Shi
Lin Chen
Wang Zhan
Yan Chen

## Slide 2: This presentation
Aims and Objectives
System Overview
Plan and Schedule
Introducing various sensing modules
Computer and Cloud interface
Challenges faced
Future prospects

## Slide 3: Aims and Objectives
Targets rehabilitation and elders care.
Health care and life care of elderly to enhance life span.
Ambient and comfortable environment.
An overview of the system
Integrated sensors via Internet of Things (IoT).
9 different kind of sensors.
Microcontroller ESP 32 with wireless data transfer via Wi-Fi.

## Slide 4: Activities of daily living
Air conditioner
Wake up
Going bed
Juicer
Microwave oven
Dish Washer
Electric Stove
Dining Chair
Water Kettle
Toaster
Kitchen
Bed Room
Bath Room
Entry/Exit
Get up in night
Using Toilet
Going Out
Shower
Hygiene
Return

## Slide 5: 3D graph

## Slide 6: System Overview
Network Administrator
Gateway
Activity Annotation
Activity Detection
Behavioural Pattern Generation
Heterogeneous Sensing system
DECISION MAKING MODULE

## Slide 7: Plan and Schedule
Fig: Gantt and Pie chart of planning and scheduling work.

## Slide 8: Implementation
Microcontroller
ESP 32 is used
  Small size
  Wireless functionality and analog inputs.
  High quality and affordable than its peers.
  Wi-Fi and Bluetooth.
  Temp. range -40 to 125C.
  Suitable for IoT applications.
  Fine grained clock gating, dynamic power scaling.
Fig: ESP 32 Microcontroller.

## Slide 9: Implementation
Current Sensor
30 Ampere ACS-712.
Software Module:
C and Python
Application:
AC, Laptop and Juicer.
Fig: ACS 712 connected with the Juicer.

## Slide 10: Implementation
Current Sensor
Fig: PCB design in Altium designer of 4 Current sensors connected with MC.

## Slide 11: Implementation
Touch Sensor
Designed using TTP223 BA6 IC, 1000 ohm resistor and 100nF capacitor.
Indigenously built.
Toggles between 0 and 1 state.
Very sensitive and efficient.
Application:
Chair, Bed, Toilet.
Fig: Touch sensor application and PCB.

## Slide 12: Implementation
Temperature Sensor
LM35 sensor.
Calibrated directly in Celsius.
Less current drain and low self heating.
Application:
Room
Fig: Circuit diagram of LM 35.

## Slide 13: Implementation
Motion Sensor
Two Grove PIR sensors used in AND gate configuration.
Works within 90 degree angle.
Detects within 5m.
Operates within 3V to 5V.
Application:
Room
Sensor 1
Sensor 2
Fig: Two Grove PIR sensors at door entrance.

## Slide 14: Interface
Computer Interface
  Python is used.
  Integrated Development Environment (IDE) Pycharm.
Fig: Chair and Juicer output.

## Slide 15: Interface
Computer Interface
  Python is used.
  Integrated Development Environment (IDE) Pycharm.
Fig: Output from Bed

## Slide 16: Interface
Computer Interface
Fig: Combine output of the sensors.

## Slide 17: Interface
Cloud interface
  Graphs generated using Thingspeak.com.
  Data is transferred in real time.
Fig: Graphs of various modules generated online.

## Slide 18: Interface
Cloud interface
  2nd Instant.
Fig: Graphs of various modules generated online.

## Slide 19: Challenges Faced
Diverse hardware and software affecting the process of integration.
Processing time gets to be distinctly pivotal.
Tremendous time consumption in finding appropriate sensors.
Sensor malfunctioning and inaccurate data transfer with delay.

## Slide 20: Future Prospects
For user friendly experience, a mobile app can be developed.
More sophisticated, commercial and aesthetically sound packaging.
Subject to monitory resources and availability of time, supplementary layer of AI can be inserted.